## Slide 1: Mbed: From a local connectivity to the cloud
Industrial Placement Presentation:
30/01/2012
Samuel Mokrani

## Slide 2: Outline
Mbed
Internet of Things
  WebSocket: new HTML5 feature
  Connecting sensors to the cloud
USB Device Stack
  USB Overview
  Stack architecture
  USB HID class
  USB Audio

## Slide 3: Mbed
Rapid Prototyping
for Microcontrollers
What is Mbed ?
Online IDE
C++ SDK
Active community
Cortex-M3 and Cortex-M0
boards

## Slide 4: Internet Of Things

## Slide 5: Internet of Things (IOT)
Physical objects addressable via the Internet
More and more devices connected to the Internet:
  15 billion by 2015 according a prediction from Cisco
Connecting microcontrollers to the Internet is the first step of the IOT:
    Smart buildings
    Medical devices

## Slide 6: IOT: WebSockets
New HTML5 feature (RFC 6455) providing:
  Full-duplex communication over a single TCP socket
  Overhead reduction
  Less traffic
  Standard and secure connections (ws:// and wss://)
Why a such new feature ?
  Replace all existing polling techniques (AJAX)
  Need a two-way communication without multiple HTTP connections

## Slide 7: IOT: WebSockets
Handshake:
GET /ws HTTP/1.1
Host: example.org
Connection: Upgrade
Sec-WebSocket-Key: dGhlIHNhbXBsZSBub25jZQ==
Upgrade: WebSocket
Origin: http://example.org
Sec-WebSocket-Version: 13
HTTP/1.1 101 Switching Protocols
Upgrade: websocket
Connection: Upgrade
Sec-WebSocket-Accept: s3pPLMBiTxaQ9kYGzzhZRbK+xOo=
HTTP request from a client to upgrade
from HTTP to WebSocket
Response from the server
Data framing:

## Slide 8: Connecting sensors to the cloud

## Slide 9: IOT: connecting sensors to the cloud
Architecture:
WebSocket Server
(Python)
Mbed board +
Sensor
(C++)
Desktop browser
(Javascript)
Mobile browser
(Javascript)
Browsers receive sensor data
  Mbed boards send sensor data to the server
  The server broadcasts each received message

## Slide 10: IOT: connecting sensors to the cloud
WebSocket server:
  Based on Tornado webserver
  ws://sockets.mbed.org/ws/<channel>/<mode>
  A client is connected over a “channel”
  Over a same channel, messages can be exchanged according the “connection mode”:
    Write-Only (wo)
    Read-Only (ro)
    Read-Write (rw)

## Slide 11: IOT: connecting sensors to the cloud
Mbed boards:
Connecting the boards to the Internet:
  Wifi module from Roving Networks:
    Full TCP/IP stack integrated
    Communication over serial port with the Mbed
  A WebSocket library on top of the TCP/IP stack
  Connection to the WebSocket server

## Slide 12: IOT: connecting sensors to the cloud
Browsers:
Architecture:
  Open a WebSocket communication with the server
  Listen WebSocket messages
  Update real-time graphs

## Slide 13: IOT: connecting sensors to the cloud
Dashboard

## Slide 14: Universal Serial Bus: Device

## Slide 15: USB Device: Overview
USB 1.0 | Low-speed Full-speed | 1.5 Mbit/s 12 Mbit/s
USB 2.0 | High Speed | 480 Mbit/s
USB 3.0 | Super Speed | 5 Gbit/s
Topology:
  One host
  Several devices
  Tiered star architecture

## Slide 16: USB Device: Overview
Transfers:
  Between “endpoints”
  Different types according to different requirements

## Slide 17: USB Device: Overview
Enumeration:
  The host sets a unique address to the device
  The host learns about the device capabilities to load an
  appropriate driver
  Device capabilities are contained in descriptors

## Slide 18: USB Device: stack architecture
Hardware abstraction
USB IRQ handler

## Slide 19: USB Device: USBDevice
USBDevice class:
  No difference between the two targets
  Enumeration step:

## Slide 20: USB Device: USB HID
Human Interface device (HID):
  Examples: mouse, keyboard, joystick
  Can be a solution to exchange raw data with a computer
  HID driver is built-in in all operating systems
  Class requirements:
    Data are exchanged in data structure called “reports”
    A report descriptor defines format and size of a report
    Interrupt IN, OUT endpoints to send and receive data

## Slide 21: USB Device: Generic USB HID device
Report descriptor includes:
  size of data: 8bits
  Lengths of input and output packets

## Slide 22: USB Device: USB Audio
Send and receive audio packets (PCM 16 bits signed) to or from a computer
Class requirements:
  Isochronous endpoints

## Slide 23: USB Device: USB Audio
Audio packets management:
  On a Start of Frame event generated each millisecond
  Packet length: according to frequency and number of channels
AUDIO LENGTH PACKET = (FREQ / 500) * nb channel

## Slide 24: USB Device: USB Audio
USB Audio tests:
  I2S/I2C DAC for the reception of audio packets
  Software to capture incoming audio packets on the host

## Slide 25: Conclusion
Internet Of Things:
  Introduction of a new HTML5 feature on embedded systems
  Connection of sensors to the cloud:
    First prototypes
    Basis for some potential IOT applications
Mbed as a USB device:
  HID: generic HID, mouse, keyboard
  Virtual serial port
  Mass Storage Device
  Audio
  MIDI

## Slide 26: Thanks! Questions ?