## Slide 1: Embedded systems: From the cloud to a global connectivity
Industrial Placement Presentation:
30/01/2012
Samuel Mokrani

## Slide 2: Outline
Mbed
Internet of Things
  WebSockets
  Connecting sensors to the cloud
  Remote Procedure Call (RPC) over WebSocket
USB Device Stack
  USB Overview
  Stack architecture
  USB HID class
  USB Audio

## Slide 3: Mbed
Lightweight Online Compiler
Cortex-M3 MCU in a Prototyping Form-Factor
Dedicated Developer Web Platform
High-level Peripheral APIs
Rapid Prototyping
for Microcontrollers
What is Mbed ?

## Slide 4: Internet of Things (IOT)
Physical objects addressable via the Internet
More and more devices connected to the Internet:
  15 billion by 2015 according a prediction from Cisco
Connecting microcontrollers to the Internet is the first step of the IOT:
    Smart buildings
    Medical devices

## Slide 5: IOT: WebSockets
New HTML5 feature providing:
  Full-duplex communication over a single TCP socket
  Overhead reduction
  Less traffic
  Standard and secure connections (ws:// and wss:// URL)
Why a such new feature ?
  Replace all existing polling techniques (AJAX)
  Allow a real server-push mechanism

## Slide 6: IOT: WebSockets
Once the connection is established:
  Messages can flow between browser and server
  No need to send a request to the server to receive a data

## Slide 7: IOT: WebSockets
Handshake:
GET /ws HTTP/1.1
Host: example.org
Connection: Upgrade
Sec-WebSocket-Key: dGhlIHNhbXBsZSBub25jZQ==
Upgrade: WebSocket
Origin: http://example.org
Sec-WebSocket-Version: 13
HTTP/1.1 101 Switching Protocols
Upgrade: websocket
Connection: Upgrade
Sec-WebSocket-Accept: s3pPLMBiTxaQ9kYGzzhZRbK+xOo=
HTTP request from a client to upgrade
from HTTP to WebSocket
Response from the server
Data framing:

## Slide 8: IOT: connecting sensors to the cloud
Purpose of this project:
  Access sensor data all over the world
  Display real-time graphs
  Using WebSockets for more efficiency
  Using the new mbed Cortex M0 board

## Slide 9: IOT: connecting sensors to the cloud
Architecture:
WebSocket Server
(Python)
Mbed board +
Sensor
(C++)
Desktop browser
(Javascript)
Mobile browser
(Javascript)
Browsers will receive sensor data
  Mbed board send in streaming to the server sensor data
  The server will broadcast each messages received
  Browsers can then read the values

## Slide 10: IOT: connecting sensors to the cloud
Mbed boards:
Connecting the boards to the Internet:
  Wifi module from Roving Networks
  Full TCP/IP stack integrated
  Communication over serial port
  A WebSocket library on top of the TCP/IP
  stack

## Slide 11: IOT: connecting sensors to the cloud
Browsers:
Architecture:
  Open a WebSocket communication with the server
  Listen WebSocket messages
  Update the real-time graph

## Slide 12: IOT: connecting sensors to the cloud
WebSocket server:
  Based on Tornado webserver
  ws://sockets.mbed.org/ws/<channel>/<mode>
  A client is connected over a “channel” and a “connection mode”
  Over a same channel, messages can be exchanged according the connection mode:
    Write-Only (wo)
    Read-Only (ro)
    Read-Write (rw)

## Slide 13: IOT: connecting sensors to the cloud
Dashboard

## Slide 14: IOT: RPC over WebSockets
Objectives:
  Execute a method on a distant mbed
  WebSocket communication
Application examples:
  Handle remotely a whole system
    Medical applications
    Mbed located in places where people cannot go frequently

## Slide 15: IOT: RPC over WebSockets
Architecture:
Mbed(s) connected to a WebSocket server
Sub-networks organization
On each sub-network, an mbed must have a unique id
JSON messages between clients and server

## Slide 16: IOT: RPC over WebSockets
Messages exchanged:
  CALL
  RESULT
  REGISTER
  INFO_METHODS
  ERROR
Messages examples:
{“from”: “mbed1”, “to”: “gateway”, “msg”:”REGISTER”, “fn”: “echo”, “id”: 10}
{“from”: “gateway”, “to”: “mbed1”, “msg”:”REGISTER_OK”, “id”: 10}
{“from”: “mbed2”, “to”: “mbed1”, “msg”:”CALL”, “fn”: “echo”, “params”: “Hello!”, “id”: 13}
{“from”: “mbed1”, “to”: “mbed2”, “msg”:”RESULT”, “res”: “Hello!”, “id”: 13}
Register method transaction
Distant method call transaction

## Slide 17: IOT: RPC over WebSockets
WebSocket server:
  Based on Tornado webserver (Python)
  ws://sockets.mbed.org/rpc/<sub-network>/<mbed_id>
  Manage all sub-networks
  Manage messages exchanged

## Slide 18: IOT: RPC over WebSockets
Mbed boards requirements:
  Wifi module or Ethernet connection
  RPC library
void echo(MbedJSONValue& in, MbedJSONValue& out)
{
out = in.get<string>();
}
int main()
{
WebSocket ws(“ws://sockets.mbed.org/rpc/net/mbed1”);
MbedJSONRpc rpc(&ws);
connectWifi();
connectWebSocket();
rpc.registerMethod(“echo”, &echo);
rpc.work();
}
int main(void)
{
WebSocket ws(“ws://sockets.mbed.org/rpc/net/mbed2”);
MbedJSONRpc rpc(&ws);
MbedJSONValue in = “Hello!”;
MbedJSONValue out;
connectWifi();
connectWebSocket();
rpc.call(“echo”, “mbed1”, in, out);
printf(“result: %s”, out.get<string>());
}

## Slide 19: USB Device: Overview
Speed:
USB 1.0 | Low-speed Full-speed | 1.5 Mbit/s 12 Mbit/s
USB 2.0 | High Speed | 480 Mbit/s
USB 3.0 | Super Speed | 5 Gbit/s
Topology:
  One host
  Several devices
  Tiered star architecture

## Slide 20: USB Device: Overview
Transfers:
  Between “endpoints”
  Different types according to different requirements

## Slide 21: USB Device: Overview
Enumeration:
  The host sets a unique address to the device
  The host learns about the device capabilities
  Device capabilities are contained in descriptors

## Slide 22: USB Device: stack architecture

## Slide 23: USB Device: USBHAL
USBHAL class:
  USB Hardware Abstraction layer for the LPC11U24 and the LPC1768
  Implemented in two different .cpp files with a unique .h
  A macro is defined by the compiler according to the target
  Low level methods:
    Write an Endpoint
    Read an Endpoint
    IRQ handler which calls virtual functions:
      EPx_OUT_callback(): data received
      Epx_IN_callback(): data sent
      SOF(int frameNumber): Start Of Frame event (each ms)

## Slide 24: USB Device: USBDevice
USBDevice class:
  No difference between the two targets
  Enumeration step for “standard” descriptors:

## Slide 25: USB Device: USB HID
Human Interface device (HID):
  primarily defined for devices that are used by humans
  Examples: mouse, keyboard, joystick
  Can be a solution to exchange raw data with a computer
  A HID driver is built-in in all operating systems
  Class requirements:
    Interrupt IN endpoint to send data
    Interrupt OUT endpoint to receive data
    Data are exchanged in data structure called “reports”
    A report descriptor defines format and size of a report

## Slide 26: USB Device: Generic USB HID device
uint8_t * USBHID::reportDesc() {
static uint8_t reportDescriptor[] = {
0x06, LSB(0xFFAB), MSB(0xFFAB),
0x0A, LSB(0x0200), MSB(0x0200),
0xA1, 0x01, // Collection 0x01
// data are sent in packets containing input length bytes
0x75, 0x08, // report size = 8 bits
0x15, 0x00, // logical minimum = 0
0x26, 0xFF, 0x00, // logical maximum = 255
0x95, input_length, // report count
0x09, 0x01, // usage
0x81, 0x02, // Input (array)
// data are sent in packets containing input length bytes
0x95, output_length, // report count
0x09, 0x02, // usage
0x91, 0x02, // Output (array)
0xC0 // end collection
};
reportLength = sizeof(reportDescriptor);
return reportDescriptor;
}
Once a report defined:
  Data can be exchanged between computer and device by writing and reading the two interrupts endpoints

## Slide 27: USB Device: USB Audio
Enable the mbed to:
  Send and receive audio packets to or from a computer
  Class requirements:
    Isochronous IN endpoint to send audio packets
    Isochronous OUT endpoint to receive audio packets
    Format of data exchanged: PCM 16 bits signed

## Slide 28: USB Device: USB Audio
Timing requirement:
  Use of the Start of Frame event generated each millisecond
  Example: reception of a 48kHz stereo stream
    Each sample is 16 bits (2 bytes) long: 48 * 2 bytes received for one channel each millisecond
    For 2 channels, 48 * 2 * 2 bytes will be received each millisecond
AUDIO LENGTH PACKET = (FREQ / 500) * nb channel

## Slide 29: USB Device: USB Audio
Implementation:
  If a user wants to read an audio packet:
    Try to read the OUT isochronous endpoint on a SOF event
  If a user wants to send an audio packet:
    Write it on the IN isochronous endpoint on a SOF event
TODO: put photo of I2S and microphone on mbed