## Slide 1: Embedded systems, Internet of Things and Communication
Industrial Engineering Internship Presentation:
30/01/2012
Samuel Mokrani

## Slide 2: Outline
Mbed
Internet of Things
  WebSockets
  Connecting sensors to the cloud
  Remote Procedure Call (RPC) over WebSocket
USB Device Stack
  USB Overview
  Stack architecture
  USB HID class
  USB Audio

## Slide 3: Mbed
Lightweight Online Compiler
Cortex-M3 MCU in a Prototyping Form-Factor
Dedicated Developer Web Platform
High-level Peripheral APIs
Rapid Prototyping
for Microcontrollers
What is Mbed ?

## Slide 4: Internet of Things (IOT)
Physical objects addressable via the Internet
More and more devices connected to the Internet:
  15 billion by 2015 according a prediction from Cisco
Connecting microcontrollers to the Internet is the first step of the IOT:
    Smart buildings
    Medical devices

## Slide 5: IOT: WebSockets
New HTML5 feature providing:
  Full-duplex communication over a single TCP socket
  Overhead reduction
  Less traffic
  Standard and secure connections (ws:// and wss:// URL)
Why a such new feature ?
  To replace all existing polling techniques (AJAX)
  Allow a real server-push mechanism

## Slide 6: IOT: WebSockets
Once the connection is established:
  Messages can flow between browser and server
  No need to send a request to the server to receive a data

## Slide 7: IOT: WebSockets
Handshake:
GET /ws HTTP/1.1
Host: example.org
Connection: Upgrade
Sec-WebSocket-Key: dGhlIHNhbXBsZSBub25jZQ==
Upgrade: WebSocket
Origin: http://example.org
Sec-WebSocket-Version: 13
HTTP/1.1 101 Switching Protocols
Upgrade: websocket
Connection: Upgrade
Sec-WebSocket-Accept: s3pPLMBiTxaQ9kYGzzhZRbK+xOo=
HTTP request from a client to upgrade
from HTTP to WebSocket
Response from the server
Data framing:

## Slide 8: IOT: connecting sensors to the cloud
Purpose of this project:
  Access sensor data all over the world
  Display real-time graphs
  Using WebSockets for more efficiency
  Using the new mbed Cortex M0 board

## Slide 9: IOT: connecting sensors to the cloud
Architecture:
WebSocket Server
(Python)
Mbed board +
Sensor
(C++)
Desktop browser
(Javascript)
Mobile browser
(Javascript)
Browsers will receive sensor data
  Mbed board send in streaming to the server sensor data
  The server will broadcast each messages received
  Browsers can then read the values

## Slide 10: IOT: connecting sensors to the cloud
Mbed boards:
Connecting the boards to the Internet:
  Wifi module from Roving Networks
  Full TCP/IP stack integrated
  Communication over serial port
  A WebSocket library on top of the TCP/IP
  stack

## Slide 11: IOT: connecting sensors to the cloud
Browsers:
Architecture:
  Open a WebSocket communication with the server
  Listen WebSocket messages
  Update the real-time graph

## Slide 12: IOT: connecting sensors to the cloud
WebSocket server:
  Based on Tornado webserver
  ws://sockets.mbed.org/ws/<channel>/<mode>
  A client is connected over a “channel” and a “connection mode”
  Over a same channel, messages can be exchanged according the connection mode:
    Write-Only (wo)
    Read-Only (ro)
    Read-Write (rw)

## Slide 13: IOT: connecting sensors to the cloud
Dashboard

## Slide 14: IOT: RPC over WebSockets
Objectives:
  Execute a method on a distant method from another mbed
  WebSocket communication
Application examples:
  Handle remotely a whole system
    Medical applications
    Not easy to access space

## Slide 15: IOT: RPC over WebSockets
Architecture:
Mbed(s) connected to a WebSocket server
Organization by sub-networks
On each sub-network, an mbed must have a unique id
JSON messages between clients and server

## Slide 16: IOT: RPC over WebSockets
Messages exchanged:
  CALL
  RESULT
  REGISTER
  INFO_METHODS
  ERROR
Messages examples:
{“from”: “mbed1”, “to”: “gateway”, “msg”:”REGISTER”, “fn”: “echo”, “id”: 10}
{“from”: “gateway”, “to”: “mbed1”, “msg”:”REGISTER_OK”, “id”: 10}
{“from”: “mbed2”, “to”: “mbed1”, “msg”:”CALL”, “fn”: “echo”, “params”: “Hello!”, “id”: 13}
{“from”: “mbed1”, “to”: “mbed1”, “msg”:”RESULT”, “res”: “Hello!”, “id”: 13}
Register method transaction
Distant method call transaction

## Slide 17: IOT: RPC over WebSockets
WebSocket server:
  Based on Tornado webserver (Python)
  ws://sockets.mbed.org/rpc/<sub-network>/<mbed_id>
  Manage all sub-networks
  Manage messages exchanged

## Slide 18: IOT: RPC over WebSockets
Mbed boards requirements:
  Wifi module or Ethernet connection
  RPC library
void echo(MbedJSONValue& in, MbedJSONValue& out)
{
out = in.get<string>();
}
int main()
{
WebSocket ws(“ws://sockets.mbed.org/rpc/net/mbed1”);
MbedJSONRpc rpc(&ws);
connectWifi();
connectWebSocket();
rpc.registerMethod(“echo”, &echo);
rpc.work();
}
int main(void)
{
WebSocket ws(“ws://sockets.mbed.org/rpc/net/mbed2”);
MbedJSONRpc rpc(&ws);
MbedJSONValue in = “Hello!”;
MbedJSONValue out;
connectWifi();
connectWebSocket();
rpc.call(“echo”, “mbed1”, in, out);
printf(“result: %s”, out.get<string>());
}